## Slide 1: Combating Combustible Dust in the Workplace
Jeff Krause
HA-International, LLC

## Slide 2: Overview
Fundamentals; getting a feel for combustible dust hazards
  Identify and classify
  Key References
Look, we’ve been doing it this way for 30-years…
Dust Hazard Analysis
Process equipment, including dust collectors and bucket elevators
Housekeeping
  Managing accumulations

## Slide 3: Identify and Classify
Material
  Often but not always organic, or metal
Small particle size, < 420 um
Flash fire or explosion when suspended in air and ignited

## Slide 4: Common combustible dusts (NOT an exhaustive list)
Agricultural products – sugars, starches, flour, whey, wood flour, powdered milk
Agricultural dusts – plant processing dusts, starches, spices, food processing dusts
Carbonaceous dusts – soot, carbon black, coal, coke
Chemical dusts – calcium stearate, paraformaldehyde, adipic acid, sulfur, many others
Textile dusts – wool, silk, synthetic fibers
Metal dusts – aluminum, bronze, magnesium, zinc
Plastic dusts – LDPE, epoxy resins, phenolic resins, melamine resins, PVA, PVC, many others

## Slide 5: Testing your material
Sampling
1-2 lb sample for full characterization, Ziploc bag typically acceptable
Collector filter, ceiling/beams, floor, equipment surfaces
Testing
Screening
Go/No Go
ASTM E1226
Explosion Severity – Kst and Pmax – needed for explosion prevention design, used for classification
Other characteristics

## Slide 6: Kst Classes
St 0 0 bar.m.s-1 Does not explode
St 1 1 to 200 bar.m.s-1 Weak explosion
St 2 201 to 300 bar.m.s-1 Strong explosion
St 3 > 300 bar.m.s-1 Very strong explosion

## Slide 7: Other tests
MIE – Minimum ignition energy
MEC – Minimum explosible concentration
Minimum autoignition temperature
Layer ignition test
Where to send the samples for analysis?
Is it okay to ship combustible dust samples?

## Slide 8: Criteria for a combustible dust explosion
Dispersion in air
  Very high concentrations, not typical process/exhaust levels
    MEC (phenolic resin) 15 g/m3
Ignition Source - MIE
  More energy needed than flammable vapors, but still can be ignited by some forms of static discharge
Dusts
  Aluminum 10 mJ
  Epoxy Resin <10 mJ
  Milk Powder 50 mJ
  Phenolic Resin 2-10 mJ
  Sugar 30 mJ
Versus Vapors
  Acetone 1 mJ
  Benzene 0.2 mJ
  Heptane 0.2 mJ
  Toluene 0.2 mJ

## Slide 9
Ignition Sources

## Slide 10: Secondary explosions
Dust is present on facility surfaces
An initial event suspends settled dust
An ignition source completes the fire triangle
Unburned dust is pushed ahead of the flame front by the pressure front in all possible directions, suspending more dust
Second explosion occurs, often much larger
Can occur inside equipment and in open areas
Dust layers over 1/64 inch thick can suspend to optimum explosible concentrations

## Slide 11: Key References
NFPA 652 – Standard on the Fundamentals of Combustible Dust
NFPA 654 – Standard for the Prevention of Fire and Dust Explosions from the Manufacturing, Processing, and Handling of Combustible Particulate Solids

## Slide 12: We’ve been doing it this way for 30-years…
Relative infrequency of dust explosions
Address credibility issues
Use incidents to trigger action
Demos can be persuasive, but be careful not to model risky behavior

## Slide 13: Prevention
Dust Hazard Analysis
Process Equipment
  Explosion relief
  Isolation
  Controlling oxygen or explosion containment may be feasible in some applications
Focus houskeeping efforts on preventing accumulations of dust-sized particles
Manage sources of ignition
  Open flames
  Static discharge
  Electrical equipment (Class 2)
  Hot surfaces

## Slide 14: Dust collectors and bucket elevators
Basic requirements
Outside building or flameless vent
Explosion relief panels
Explosion Isolation Valve

## Slide 15: Retrofitting dust collectors
Select relief vents to fit between reinforcing ribs for easy installation
Consider pneumatic nibbler and punches to allow installation without rebagging

## Slide 16: Housekeeping
Manage accumulations
  Consider painting flooring surfaces to highlight visible dust
  Should always be able to see the floor color
Never “blow down” the process
Use vacuum systems rated for combustible dusts, or hand brushes & brooms
  Consider fixed vacuum systems for areas requiring frequent cleaning
  Go after dust escape points aggressively

## Slide 17: Worker training topics
Hazard awareness
Preventive measures
Inspection & reporting
Housekeeping methods
Special firefighting considerations
  Fire extinguishers may suspend settled dust

## Slide 18: Questions or comments?